STM32H735G_DK

# Code deployment.
## Fedora system setup.
### ‘dnf install openocd’
### ‘dnf install telnet’
### ‘dnf install g++’
### ‘dnf install arm-none-eabi-gcc-cs’
### ‘dnf install arm-none-eabi-gcc-cs-c++’
### ‘dnf install arm-none-eabi-newlib’
## Build Makefile.
### Run each time after adding / removing / moving source files from a terminal at ‘STM32H735G_DK’.
### ‘make/build_makefile.sh targets/target_name.target > /dev/null’
### ‘target_name’ is one of:
#### ‘ALL_735H’
#### ‘TOUCH_SCREEN_STM32H735’
#### ‘TEST_SDRAM_STM32H735’
#### ‘TEST_FLASH_STM32H735’
#### ‘BASIC_STM32H735’
## Compile.
### Run from a terminal at ‘STM32H735G_DK/bin’:
### ‘make -j8’
## Chip burning.
### Refer to the openocd doc file.

## TouchScreen.
### For building the touch screen demo, build the makefile using ‘TOUCH_SCREEN_STM32H735.target’ (or ‘ALL_735H’).
### The touch screen demo application uses leds, sdram, lcd, and touch screen. After burning the demo, you can follow a single, or double touches on the lcd screen. In case of triple touch, the code asserts (for demonstrating the assert mechanism).
## UsbDevice.
### For building the usb mouse device demo, build the makefile using ‘USB_STM32H735.target’ (or ‘ALL_735H’).
### The usb device demo application uses leds, sdram, lcd, and touch screen. After burning the demo, you can connect a mouse to ‘USB FB’ connector. Left button moves mouse faster. Right button moves mouse slower.
# Makefile.
## Makefile generating code.
### Directory ‘make’ holds the makefile generating code, and scripts. That code is not documented.
### Code is divided to libraries, and modules.
### A library directory holds a file named ‘library.params’.
### A module directory holds a file name ‘files.make’.
### The only exception is the main directory, which is both a library, and a module. It is also a module that receives the list of active modules (using the compiler -D option for params definition).
### When adding a file to repository, you must add it to the ‘files.make’ list.
### When adding a directory to the tree, you must add it also in the parent module / library.
### Common compiler directives are to be found in ‘target/XXX.compiler’. (One such parameter is ‘-D ASSERT_LEVEL_ACTIVE=0x30U’ in ‘target/ARM_GPP_DEBUG.compiler’).
### The code generates a single ‘Makefile’ at ‘STM32H735G_DK/bin‘. This makefile is mostly parallel, so we can use the ‘make -jx’ command effectively.
# Directories structure.
## Layout.
### All source directories come under ‘src’ path.
### Directory ‘src/COMMON’ holds the common files libraries. These are the files that are platform independent, and application independent.
### Directory ‘src/PHYSICAL’ holds the chip specific libraries. As an example, we have the ‘src/PHYSICAL/STM32H735’ library for the STM32H735 chip. Here you can find mostly registers related code.
### Directory ‘src/PLATFORM’ holds the platform specific libraries. As an example, we have the ‘src/PLATFORM/DISCOVERY_735G’ library for the STM32H735G-DK board. Here you can find mostly actual gpio related implementations.
### Directory ‘src/APPLICATION’ holds the actual applications related code.
### As a simple example, consider the I2C objects. ‘I2cMaster’ is a ‘COMMON’ member, mostly for defining the interface. ‘H735I2cMaster’ is a ‘PHYSICAL’ member, implementing the interface. ‘Disc735I2cMaster4’ is a ‘PLATFORM’ member, which initializes the i2c gpios for i2c4.
### Libraries usually have a ‘redirect’ path, for ease of use. We use the typedef directive for the chip dependent, and platform dependent files. A chip depended is prefixed by ‘Physical’ (i.e. the ‘H735I2cMaster’ file adds a typedef directive to ‘PhysicalI2cMaster’, and redirected by ‘PhysicalI2cMaster.h’ in the redirect path). For platforms dependent code we employ the ‘Platform’ prefix.

# Coding conventions.
## Naming conventions.
### For objects (class, struct, enum, typedef), we use a capital letter heading each word (followed by lower case). For example – ‘ModuleManager’.
### Each file holds a single object. The filename is the same as the object name. (So the filename for the ‘ModuleManager’ object is ‘ ModuleManager.h’).
### C++ implementations filenames are terminated by ‘.cc’.
### Assembler implementations filenames are terminated by ‘.a’.
### Defined directives are all capital (such as ‘ASSERT_CRITICAL’).
### Variables are all lower case (such as ‘range_start’).
### Class member variables are prefixed by ‘m_’ (such as ‘m_flash_manager’).
### Class global variables are prefixed by ‘g_’ (Such as ‘g_ticks_count’).
### Method, and function names are a lower cased word, followed by capital headed word (such as ‘getClockControl’).
## Asserts.
### ‘ASSERT_TEMP’ – used during development for bug hunting. Should not be present in the code.
### ‘ASSERT_DEV’ – used for testing any assumption that is always valid on wakeup (such as offset of a variable in a register structure).
### ‘ASSERT_TEST’ – used for testing any state that may happen according to user actions, but would not cause an erroneous system behavior. It may still cause a system crash, such as a NULL pointer access.
### ‘ASSERT_CRITICAL’ – used for identifying any possibly erroneous behavior. (an example would be unhandled case in a switch clause).
## Switch cases.
### When possible, use explicit case for each possible value, so that the compiler would issue a warning on any new (missing) case.
## Inheritance.
### This code prohibits multiple inheritance.
### Only exception is the module managers, that may implement multiple pure virtual interfaces.