Usb Manager

# Modules.
## UsbManager.
### File ‘PHYSICAL/STM32H735/system/stm32h735.ld’ sets ‘resetHandler’ as the entry code.
## UsbChannelsManager.
### ‘APPLICATION/APP_STM32H735/basic_stm32h735.cc’ implements the ‘main’ function.
# UsbChannelSingle.
## General.
### The channel class is a state based object.
### Each channel instance must be a member of a single device, with the exception of the main control channel, which is a member of UsbEnumerator.
### Channels may be of several types:
#### ‘UsbChannelSingleControl’ – A special channel that implements both input and output. Each transaction has two phases. First phase is sending an 8 bytes standard control query. Second phase is receiving the device reply.
#### ‘UsbChannelSingleInterrupt’ – An input channel that queries device periodically.
#### ‘UsbChannelSingleBulk’ – An output channel that sends packets to devices.
### A state change may be triggered by an interrupt action, a user request, or a port error.
### Each transaction is initiated by the owner device. The device sets up the transaction parameters, but does not start the transaction.
### Each channel tries to send / receive one packet each frame, until the transaction terminates.
### During transaction setup, the device determines how many frames to wait before transaction initiates. This delay must be at least 1 frame. Used mainly by interrupt transactions.
### The frame delay is also a main synchronization component between the main process, and the interrupts handler.
### .
## State ‘USB_CHANNEL_STATE_CLOSED‘:
### In this state the channel is detched, and can do no action.
### The channel is managed only by the owner device.
## State ‘USB_CHANNEL_STATE_DISABLED‘:
### In this state the class instance is attached to a distinct channel.
### The instance has no transaction active.
### All channel generic parameters are set in the core registers.
### The channel is managed by both the owner device, and the channels manager.
### The owner device can initiate any valid transaction. Moves to state ‘USB_CHANNEL_STATE_ACTIVE’. Sets up the transaction parameters. Set the frame delay to a positive value. Unmask the respective channel interrupts.
### Both the owner device and the channels manager can detach device. Moves to state ‘USB_CHANNEL_STATE_CLOSED’.
## State ‘USB_CHANNEL_STATE_ACTIVE‘:
### This is the transaction active state.
### This state is managed by the interrupts handler. The exception is detaching the channel due to device error, or port error.
### In this state the class instance is attached to a distinct channel.
### The channel class is a state based object.

### USB_CHANNEL_STATE_ACTIVE, USB_CHANNEL_STATE_NACK, USB_CHANNEL_STATE_OUT_READY, USB_CHANNEL_STATE_IN_READY, USB_CHANNEL_STATE_ERROR
### .
### The channel class is a state based object. Hence it has a main ‘tick’ method that decides what action to take based only on the current state.

# UsbPortManager.
## States.
### The port manager is a state based object.
### All state changes are done through the main process using the ‘tick’ method.
### State ‘USB_PORT_POWERED_DOWN’:
#### Disable the external usb power supply.
#### Powered down state disables the usb board power regulator. The usb power may remain high if a connected device has internal power source.
#### Power down state is active for 1 second, after which we automatically move to ‘USB_PORT_DISCONNECTED’
### State ‘USB_PORT_DISCONNECTED’:
#### Waits for a device connection.
#### When a device is connected, move state to ‘USB_PORT_ENUMERATION_PENDING’, with timeout of 100 ms (before initiating enumeration process).
#### When detecting over-current on the usb power, move state to ‘USB_PORT_POWER_DOWN_PENDING’.
### State ‘USB_PORT_ENUMERATION_PENDING’:
#### Enumeration pending is active for 100 ms, after which we automatically initiate the enumeration process.
#### When detecting over-current on the usb power, move state to ‘USB_PORT_POWER_DOWN_PENDING’.
### State ‘USB_PORT_RESET_ACTIVE’:
#### Wait for an external trigger to clear the reset signal and move to ‘USB_PORT_CONNECTED’ state.
#### When detecting over-current on the usb power, move state to ‘USB_PORT_POWER_DOWN_PENDING’.
### State ‘USB_PORT_CONNECTED’:
#### Wait for a channel enable signal.
#### If channel is enabled, move state to ‘USB_PORT_ENABLED’.
#### When detecting over-current on the usb power, move state to ‘USB_PORT_POWER_DOWN_PENDING’.

### State ‘USB_PORT_ENABLED’
#### Important – this is the only state where the usb interrupts are active.
#### When an enabled device enters a logical error state, it would physically disable the port.
#### Immediately after entering the enabled state, unmask usb interrupts.
#### Prior to leaving the enabled state, mask usb interrupts.
#### If detecting a physical disable action, move to ‘USB_PORT_POWER_DOWN_PENDING’.
#### When detecting over-current on the usb power, move state to ‘USB_PORT_POWER_DOWN_PENDING’.
### State ‘USB_PORT_POWER_DOWN_PENDING’
#### Disable the external usb power regulator.
#### Wait for an external notification that all channels are closed.
#### When all channels are closed, move to ‘USB_PORT_POWERED_DOWN’ with timeout of 1 second.